Assumptions:
1. Input tensor much larger than #MAC units available.
2. Weights and activations are stored in memory uncompressed.
3. Goal is to optimize memory accesses regardless of spatial unrolling techniques or #MAC units.
4. Input tensor is not padded, FSM control loop has to keep track of weights used.
5. AI SoC accelerates Conv2D.
6. Applications don’t fit in on-chip memory.

Notes:
1. Each filter element is used 64x64 times.
2. Each activation element is used 32x9 times (at most N positions of an N dimensional kernel).

Design choices:
1. Weight and output stationary approach. 1 filter at a time is convolved with the input.
2. Weights + inputs are stored in the RF for a total of 231 words. Full 1 filter + FIFO the size of iterations after which each activation element can be discarded because no longer used.
3. Idea is to start from having (multiple) of 36 MACs for producing 1 output pixel.
4. Output stored directly to DRAM.
5. Choice of orchestration/zoo keeping of SIMD MAC arrays instead of systolic array due to impact of sparsity on its utilization which decreases geometrically in realistic DNN workloads, making systolic arrays idle. At the same time, orchestrated/scheduled SIMD MAC arrays can be utilized completely by scheduling data into it from multiple separate convolution or matrix-multiply operations.